## Slide 1: Measurement-Augmented Spectrum Databases for White Space Spectrum
Ayon Chakraborty and Samir R. Das
Stony Brook University
WINGS Lab

## Slide 2
TV White Space Primer
WINGS Lab
RSS Threshold
Snapshot of the TV Spectrum in Stony Brook, New York.
White Space
FCC opened up this spectrum band for unlicensed use in 2008.
6MHz channels

## Slide 3
TVWS Availability as a Service
WINGS Lab
TVWS
Database
Location: (X,Y)
Estimated WS channels: [23, 34, 41]
Secondary
User
Some official TVWS database vendors in the United States:

## Slide 4
Current Databases are Erroneous
WINGS Lab
TVWS
Database
Location: (X,Y)
Estimated WS channels: [23, 34, 41]
Secondary
User
Ground Truth WS channels: [34, 41, 29, 43]
False Negatives
False Positives
Revealed by spectrum sensing at (X,Y)

## Slide 5
≈75% of Available WS is Lost!
WINGS Lab

## Slide 6
Cause: Poor propagation models
WINGS Lab
Real Protection Contour
(or service area)
Estimated Protection Contour
(by TVWS Databases)
Secondary User
Lost white spaces translates to wasted bit capacity

## Slide 7
Fixing Errors – Intuition
WINGS Lab
Identify regions where database is prone to make more errors.
Do actual measurements
Use DB propagation model estimates
Interpolate rest of the locations

## Slide 8
True +ve/-ve
The Classifier
WINGS Lab
<geo-spatial features><label>
<geo-spatial features><label>
<geo-spatial features><label>
<geo-spatial features><label>
<geo-spatial features><label>
Training data
Classifier Model
<geo-spatial features>
False +ve/-ve
Use TVWS DB
Use Measurement
A Decision Tree Classifier works best for our system.

## Slide 9
Geo-spatial Features
WINGS Lab
1. Line-of-Sight Obstruction Length
(NASA SRTM Terrain Data)
Receiver location
Transmitter location

## Slide 10
Geo-spatial Features
WINGS Lab
(From TVWS DB using propagation models)
2. Estimated Power
Receiver location
Transmitter location

## Slide 11
Geo-spatial Features
WINGS Lab
3. Distance from Transmitter
Receiver location
Transmitter location

## Slide 12
Classifier Label
WINGS Lab
Location: X,Y
Ground Truth WS Availability
Estimated WS Availability
Measurements using ThinkRF spectrum sensor
Obtained from Spectrum Bridge TVWS Database
True +ve/-ve
False +ve/-ve
Match?

## Slide 13
Collecting Ground Truth Data
WINGS Lab
East New Jersey area (approx 250 sq. Km)
Suffolk and Nassau counties, Long Island (approx 150 sq. Km)
30 DTV channels, 150K+ data points obtained spread across 5K+ locations.

## Slide 14
Performance of the Classifier
WINGS Lab
With ≈10% training data classifier accuracy is ≈80%
The classifier based in a different geographical region performs only incrementally worse than that based in the same region.

## Slide 15
Effort vs. Accuracy
WINGS Lab
Measurement Effort
0%
100%
Model Based
Dense Measurement
Low
High
Prediction Accuracy
Exhaustive
Measurement
FCC F-Curve
Longley-Rice
Mobicom’14
HotNets’13
Opportunistic Measurement
(This work)

## Slide 16
Performance
WINGS Lab
Measure Random points + TVWS in rest
Measure Random points + interpolate in rest

## Slide 17
The Big Picture
WINGS Lab
DB grossly erroneous
DB grossly ok
More patchy

## Slide 18
Summary
WINGS Lab
TVWS databases produce erroneous estimates leading to significant loss of usable WS spectrum.
Direct spectrum measurements can remedy this problem but requires significant effort.
We developed a classifier approach that reduces this effort by using measurements only in regions where the databases are likely to be inaccurate.
Overall, significant improvement in accuracy with only modest measurement effort.

## Slide 19
EOF
WINGS Lab

## Slide 20
Demand vs. Availability
WINGS Lab
Los Angeles (0)
San Francisco(3)
Seattle(4)
Chicago (3)
New York City (1)
Atlanta (5)
Houston (3)
Philadelphia (2)
Map from “How much white space is there?” (Anant Sahai et. al.)
Big population hubs are scarce in white space availability where spectrum demands are the highest.
Availability data from Spectrum Bridge